| Date of Thorough Examination: July 14, 2021 | Date of Report: July 14, 2021 | Report number: RPXXXX |
| --- | --- | --- |

| P.O.Number: 205102 (line 1) | RFI Number: RFI-21-140 |
| --- | --- |

| Name and Address of employer for whom the thorough examination was made: PT. Vetco Grey Indonesia, Jl. Kerapu No. 14 & 15 Industrial Sector Batu Ampar, Batam | Address of premises at which the examination was made: PT. Rigspek Perkasa Komplek Kawasan Industri Sekupang, Kav. No.13, Batam 29428 - Indonesia |
| --- | --- |
| Description and identification of the equipment: | Safe Working Load(s): | Load test applied | Date of manufacture if known: | Date of last thorough examination: |
| Sling, 26 mm Dia., 1 x 8.3 tons SWL, wire rope gradeb1770 (6x36 IWRC Galvanised), C/W two soft loops (400 mm eye length, 200 mm eye Dia.) Mechanically spliced at both ends and one bulldog clip (forge type), 40 ft effective LG. Sling ID : RP-TI 2284 Previous sling ID : FML 8510 H Note : Proof Load Using Load Cell 25T S/N: 23391 Previous PO No. : 203516 P/N No. : R300185-71 REV A NCR No. : NCR74860 Previous Inspection Report No. FOI-ISD-C2344 Acceptance criteria : AS 1666.1 “Wire Rope Sling – Production Specification” | 8.3 tonnes | 16.6 tonnes 2 x SWL (5 minutes holding time) | unknown | December 30, 2019 |
| Is this the first examination after installation or assembly at a new site or location? |  | Was the examination carried out: |
|  | YES | - | NO | - | Within an interval of 6 months? | YES | √ | NO | - |
|  |  | Within an interval of 12 months? | YES | - | NO | - |
| If the answer to the above question is YES has the equipment been installed correctly? | YES | - | NO | - | In accordance with an examination scheme? | YES | - | NO | - |
|  |  | After the occurrence of exceptional circumstances? | YES | - | NO | - |
| Identification of any part found to have a defect which is or could become a danger to persons and a description of the defect: (If none state NONE) : NONE |
| Is the above a defect which is of immediate danger to persons | YES | - | NO | √ |
| Is the above a defect which is not yet but could become a danger to persons: (If YES state the date by when) | YES by: - |
| Particulars of any repair, renewal or alteration required to remedy the defect identified above: NONE |
| Particulars of any tests carried out as part of the examination: (If none state NONE) NONE |
| IS THIS EQUIPMENT FIT FOR PURPOSE? | YES | √ | NO |  |
| Name & Qualifications of person making this report: Josua Sahat Sinaga Lifting Gear Inspector | Name of person authenticating this report: Doharmin Manik Testing and Inspection Supervisor | Latest date by which next thorough examination must be carried out: Visual Inspection - January 13, 2022 Load Test – July 13, 2022 |