| Date of Thorough Examination: September 24, 2020 | Date of Report: September 24, 2020 | Report number: |
| --- | --- | --- |

| P.O.Number : | RFI Number: RFI-20-134 |
| --- | --- |

| Name and Address of employer for whom the thorough examination was made: Baker Hughes a GE Company | Address of premises at which the examination was made: PT. Rigspek Perkasa Komplek Kawasan Industri Sekupang, Kav. No.13, Batam 29428 - Indonesia |
| --- | --- |
| Description and identification of the equipment | Safe Working Load(s) | Load test applied | Date of manufacture if known | Date of last thorough examination |
| Single Leg Wire Rope Sling Dia. 20 mm Dia x 40 ft Length, 6x36 IWRC EEIPS Galvanized Steel Wire Rope, Both End Mechanical Spliced with Soft Eye (Eye Dia:12”) Fitted with 2 Ea Crosby Bulldog Wire Clip G450. Size ¾”. ID : RP-P 0877 P/N : R300185-45 REV NC Note : Visual Inspection Acceptance Criteria: AS 1666.1 | 4 MT | 8 MT 2 x SWL (5 minutes holding time) | October 10,2019 | - |
| Is this the first examination after installation or assembly at a new site or location? |  | Was the examination carried out: |
|  | YES | - | NO | - | Within an interval of 6 months? | YES | √ | NO | - |
|  |  | Within an interval of 12 months? | YES | - | NO | - |
| If the answer to the above question is YES has the equipment been installed correctly? | YES | - | NO | - | In accordance with an examination scheme? | YES | √ | NO | - |
|  |  | After the occurrence of exceptional circumstances? | YES | - | NO | - |
| Identification of any part found to have a defect which is or could become a danger to persons and a description of the defect: (If none state NONE): NONE |
| Is the above a defect which is of immediate danger to persons | YES | - | NO | √ |
| Is the above a defect which is not yet but could become a danger to persons: (If YES state the date by when) | YES by: - |
| Particulars of any repair, renewal or alteration required to remedy the defect identified above: NONE |
| Particulars of any tests carried out as part of the examination: Proof Load Test Report No: TB8752 |
| IS THIS EQUIPMENT FIT FOR PURPOSE? | YES | √ | NO |  |
| Name & Qualifications of person making this report: Josua Sinaga Lifting Gear Inspector | Name of person authenticating this report: Rio Sintong Immanuel Testing and Inspection Supervisor | Latest date by which next thorough examination must be carried out: March 23, 2021 |